Detalle del Equipo para Seguridad

Marca: OEM

http://www.oem.com/

### Contenido del Paquete:

- 4 X 24 IR Waterproof  Color Cameras (Impermeable)

- 1 X 4 Channel PC Based 50/60fps DVR Card

- 4 X Power Supplies

- 4 X 9m Video Cables

- 4 X Mounting Brackets

- 1 X Software CD

### Características de las camaras:

- LED :24 LEDs

- Infrared Imps : More than 9m

- Infrared Wave length : 850m

- Image Device : 1/4" SHARP Exview HAD CCD

- Horizontal Resolution : 420 TV Line

- Picture Elements PAL: 500(H)*582(V) / NTSC: 510(H)* 492( V)

- System of signal : PAL/NTSC

- Minimal Illumination : 0.000 LUX(infrared lamps turn on)

- S/N Ratio : More than 48dB

- Camera characteristic : 0.45

- Electronic Shutter : 1/50(1/60)-1/100.000Sel

- Video Output : 1.0 VP-P750hms.Negative

- Power Consumption : 12VDC.120mA ( When the infrared lamps turn on maximum electricity in 400mA)

- Built-in Lens : 6mm

### Características de la tarjeta:

- MPEG4 software compression

- Display and record resolution 320X240/352X288

- 1-4 channels video input 40f per card. Max 4 cards

- 1 channels audio input from sound card

- 1 channel analog switch output

- Max 2 channels audio input

- 120M/h-150M/h hard disk place

### Requerimientos para la instalación:

- OS: windows 2000/XP

- CPU: P3 1G or higher

- Memory: At least 128M of RAM (256M required for 16 cameras)

- Hard disk: 80G

- Mother board: Based on Intel 815/845 chipset or higher.

- VGA card: ATI RAGE 128 or higher

- Windows Directx8.0 or above

### Garantía del Servicio:

- Cuenta con un año de garantía.

- Se garantiza que el equipo es totalmente nuevo.

- Se cambiara el equipo o se devolverá el dinero según sea su decisión en caso de presentar problemas de fabricación.

- Al finalizar el año de garantía puede ser expandible a otro año con un cargo adicional.

Ing. Rogelio García Sanabria

IT Administrador.

Tel.: 864-3846 /    537-1367